## Slide 1: TelCal Phasing Engine description
Draft
Robert Lucas
2012-12-07

## Slide 2: Inputs
Source model, TBD form:
  List of point-source components (from e.g. a cleaned map)
  Visibility uv data
Previous scan’s data (ASDM)
  Channel averaged data
  WVR data
  Full resolution data is not used.

## Slide 3: Output
WVR coefficients (WVR engine)
  May be not on every scan (if one 30s subscan per scan)
Phase correction to be applied (next scan)
  For each antenna, baseband.
Quality control
  based on correlation of the phased output with test antenna.

## Slide 4: Processing (1)
Normal WVR engine
  Its output is used by the correlator to implement the fast loop,
  The correlator applies the correction to the LO4 phases, not to the data as delays.
  Nothing to do in TelCal (implemented)
  May be not necessary every scan.

## Slide 5: Processing (2)
Phasing engine
  Implements the slow loop, in TelCal
  Compute, from source model, the model visibilities during previous scan.
  Divide observed visibilities by the model ones
  Solve from antenna gains:
    Weights as usual (1/Tsys**2), the test ant gets the sum of weights of all others
    Antenna amplitudes (efficiencies) can be used for quality control
    Antenna phases are the desired main output, they are the error in the correction Delta_psi that was applied previously
  New corrections are Psi_new = Psi_old + Delta_Psi
  Initiate the process with zero correction Psi_old=0
  Need to keep track of the previous correction (in previous result).

## Slide 6: Processing (3)
Evaluate efficiency:
  The phase correction increments should be small (slow instrumental phase drifts, after the first scan)
  Assuming that one of the correlator inputs is not a real antenna, but the sum of the others:
    The amplitude gain on the test antenna should be N times that of the others (its noise is root(N) larger)
    The amplitude gains on all other antennas should be equal (detect pointing, focus errors, decorrelation for large baselines)

## Slide 7: Needed changes in infrastructure
Enumerations:
  add one intent, a result type, …
Add a CalResult table in ASDM (e.g. CalPhasing or CalVLBI)
  New antenna phase corrections /antenna, baseband
  Antenna amplitude gains, for quality control
  Need to define this early (but should be OK as these are only additions). More difficult to change afterwards so do not make mistakes or omissions.

## Slide 8: Existing parts
WVR engine (no changes needed in TelCal)
  Recent experiments validated the on-line correction…
Antenna gain solver
  Exists and is used in many TelCal engines.

## Slide 9: New parts
Description of new table for ASDM model
  Input to the UML model is needed for code generator.
Model visibility calculation
  Calculate u,v for each baseline
  Interpolate input uv image to these u,v;
  or
  DFT of input map multiplied by primary beam.
Fill output table with phase corrections & amplitude gains
  Compute gain ratio for test antenna.

## Slide 10: Testing
Need some real data, and the model for this data
  The model can be built by calibration and imaging these same data (!), the calibration gain table can be used as a comparison later;
  A point source (quasar) is a good start (no model needed); hopefully get some real data on the true target (SciVer data band 3 and 6 are available…)
Test the engine on the uncalibrated data
  The output corrections should match the calibration gain table, for each scan taken individually
We need a utility (like applyWVR) to simulate the correlator actions in the input asdm
  Apply the WVR corrections as phase commands, not as pathlength corrections
  Apply the phase corrections.
  Tthe correction should be ~0 after a few scans when the utility has been run on the previous scans
  That utility could, may be, add the test antenna to the asdm.
Need to plot result: phase corrections vs time and antenna gains vs time