Last modified: Tues Apr 10 07:30:43 2007

## EVN CBD Critical Design Review on DBBCs

### Question Areas and Questions (in no particular order)

Later additions are coloured RED

- Context

  - What are the short term, medium term and long-term ambitions of
the EVN? (short < 2 years, medium 2-4 years, long > 4 years)

  - What are the short-term needs of the EVN? e.g. for replacements or
provisioning.

  - Are NRAO and NSF committed to VLBA enhancements?

  - What about the geodetic community?

  - Are the designs going to be freely available (bitfiles, PCB
artwork, etc. but NOT the tools or, possibly, some of the IP)?

  - Are there "hidden" or proprietorial aspects?

- Performance

  - What can it do? Take Mark 4 capabilities as a reference.

  - More detailed questions from Dick Ferris

    - Specifications

General:

- Input frequency bands:  0-512,512-1024,1024-1536,1536-2048

- Tuning resolution :  (1024MHz)/(2^32)

- Output bandwidth(s) :  0.5,1,2,4,8,16 U&L, 32 I&Q, 512 MHz

- Output data format(s) :  as MK4 sampler adapter or VSIC in geo and VLBA mode

- Frequency reference : 10 MHz

- Time reference : 1PPS

Features possibly included:

- Input band inversion? no at present, possible

- Output sideband inversion?  no at present, possible

- Phase continuous frequency switching?  yes

- Automatic return to exact signal phase after complete restart? yes

- Automatic return to exact sample time after complete restart? yes

- Input AGC servo? yes

- Output level/statistics servo? yes

- DC offset servo? manual

- IF reconstruction DAC? yes

- High resolution data output? yes

- Cal tone extraction? no, because provided by MK5B, possible

Others?

- Monitor points: through monitor bus + DAC

- Input level? nominal -8 dBm, with additional internal amplifier -30 dBm

- Output level (2-bit statistics)? yes, with automatic loop control

- Frequency and time reference signal? yes, out VSI data clock and 1PPS

- Clock jump? monitored

- Power supply voltages? monitored by PCSet

- Chip temperatures? monitored by PCSet in the Core2, internal air flow temperature

- Fan failure? no direct, as internal air flow temperature

- PLL loop voltage? synthesizer monitored by PCSet

- Servo loop control signals? ?

Others?

Detailed Specs

ADC antialiasing filters:

- Pass band: +-1 dB

- Transition band:  -15 dB

- Stop band: -50 dB

ADC:

- Sampling frequency: 1024 MHz, others possible

- Resolution bits: 8 bit, 10 bit with ADB2 in piggy-back connectors

- CW saturation level (FSD): -2 dBm

Noise floor

- ADC noise, quantising and thermal:

- Clock jitter noise per signal frequency:

- Arithmetic (rounding) noise referred to ADC, per bandwidth

- Spurious responses:

- Normal operating level :

all depending on the device, see datasheet of Max108 and ATMEL AT84AS008

Mixer:

- LO resolution bits:  32 bit

- Spurious responses: <

- Sideband separation: > 50 dB

IF filters, per bandwidth:

- Pass band: at present simulates analog filters

- Transition band: at present simulates analog filters, -6dB

- Stopband: better than 45 dB

- Ratio of integral stopband/integral passband: ?

- CW saturation level referred to ADC: +6 dB with respect to ADC saturation

AGC, DC offset and/or output resampling servos if fitted: data not available at this time

        - Control range

        - Loop stability with Gaussian noise input over range

        - Loop stability in presence of strong CW signal (RFI)

Frequency and time reference signals:

- Signal format: LVCECL/LVDS

- Signal levels: Internal 3.3, 2.5V, external LVDS 3.3V

- Terminating impedance: 100 ohm

Power supplies

- Voltages: internal 12, 5, 3.3, 1.5, -5 V, external 110/220 VAC, std 1U PC

- Tolerances: depending on the rail

- Loads: about 300W, high load switching on

Mechanical

      - Size: 19”, 8U, 500 mm

      - Mounting: 19” rack

      - Cooling: front-rear, tangential fan

      - Shipping weight: about 25 Kg

Documentation : no documentation at present, shortly prepared for O’Higins

      - Engineer:

        - Design

        - Implementation

        - Diagnostics

        - BOM

      - User:

        - Installation

        - Test and verification

        - Operation

        - Diagnostics

Control software

- Stand alone: yes

- Field System interface: yes

  - What can it not do?

  - How frequently have missing capabilities been requested?
See here for some information about EVN scheduling history.

  - What expansion/enhancement potential does it have?

  - How does it integrate with recording and networking?

- Operations

  - What does it connect to (at both ends)?

  - What "knock-on" consequences does it have? e.g. changes to the
field system and operational aspects such as dynamic firmware
changes.

  - Have these knock-ons been factored into the planning?

  - Are delay changes with bandwidth compensated?

  - If the configuration is cycled, does phase recover?

  - Do the FPGAs need "setting up" after configuration?

  - Are there built in calibration procedures?

  - Will parameter/temperature drifts require recalibrations?

  - How long does reconfiguration take?

  - How long would recalibration take?

  - Is the field system enough or is another processor/driver required?

  - How are the input "power" levels monitored and controlled?

  - How are the output "power" levels monitored and controlled?

  - Are mixed operations, i.e. old and new, possible/convenient?

  - Are there other impediments to either, DBBC/DBE2 solution?

  - Is phased deployment, e.g. DBBC early, DBE2 late, feasible?

  - Is phase cal practical, necessary, convenient?

  - Are there obsolescence-prone or risky parts?

- Manufacture

  - Are extensive manual calibration procedures required?

  - Is there a suite of tests?

  - How far advanced is it? Can production begin?

  - What plans are there for production?

  - What are the timescales?

- Costs

  - What are the costs?

  - How do costs vary with quantity and phasing?