ALMA Phasing Project Maintenance Manual

ALMA-05.11.10.05-0001-A-MAN

Version: A

Status: Draft

2014-12-8

| Prepared By: | Organization | Signature and Date |
| --- | --- | --- |
| R. Lacasse Geoff Crew Alejandro Saez M. Honma | NRAO Haystack Observatory JAO NAOJ |  |
| Approvals: |  |  |
| TBD | Haystack NRAO Japan ALMA SE ALMA PA ALMA Safety |  |
| Release: |  |  |
| TBD (NRAO Proj. Mgr.) TBD (JAO. Proj. Mgr.) | NRAO JAO |  |

Change Record

| Version | Date | Affected Section(s) | Change Request # | Reason/Initiation/Remarks |
| --- | --- | --- | --- | --- |
| A | 2014-9-5 | ALL | None | First Issue |
| A01 | 2014-12-01 | TOC | None | Updated table of contents |
| A02 | 2014-12-08 | Several sections | None | Add references to modules-level maintenance manuals. Add costs. Add system-level maintenance procedure. |

Table of Contents

1	Description	5

1.1	Purpose	5

1.2	Scope	5

2	Applicable Document, Reference Documents, Acronyms and Definitions	5

2.1	Applicable Documents	5

2.2	Reference Documents	6

2.3	Abbreviations and Acronyms	6

2.4	Definitions	7

3	ALMAPhasing System Description	8

3.1	System Overview	8

3.2	H-Maser	8

3.3	Phasing Interface Card	11

3.4	Fiber Mux and Fiber Demux	12

4	Module-level maintenance procedures	13

5	System-level maintenance procedures	13

6	Expected Maintenance Costs	14

List of Figures

Figure 31.  Block Diagram of the ALMA Phasing System.	10

Figure 32.  Photo of the H-Maser	11

Figure 33.  Photo of a PIC.	12

Figure 34.  Photo of the Fiber Mux and Fiber Demux.	13

# Description

## Purpose

This ICD covers the maintenance requirements of and procedures for the equipment supplied by the ALMA Phasing Project.   It also provides the expected costs of the maintenance activity.

## Scope

The ALMA Phasing Project is identified in the following document: [AD 01].  This document provides a general overview of the system for the benefit of those who need to maintain it.  It also includes or references plans and procedures for maintenance of all the equipment supplied to ALMA by the ALMA Phasing Project.  Finally, costs associated with maintenance are provided.

# Applicable Document, Reference Documents, Acronyms and Definitions

Applicable documents are necessary for the understanding of this document.  In some cases, they provide additional requirements which are to be incorporated into the ICD.  Reference documents are supplemental and simply provide further reference for various topics. In most cases, the acronyms used in this document are consistent with ALMA defined acronyms, however additional acronyms have also been listed which are outside the scope of ALMA definitions. No distinction is made between these two uses.

## Applicable Documents

The following documents, of the exact issue shown, form part of this document. In the event of conflict between the documents listed here and this document, this document shall take precedence.

| Number | Document Title | Reference |
| --- | --- | --- |
| [AD 01] | ALMA Product Assurance Requirements | ALMA-80.11.00.00-001-C-GEN |
| [AD 02] | ALMA 64-Antenna Correlator Safety Hazard and Risk Analysis Report | ALMA-60.00.00.00-057-A-REP |
| [AD 03] | ALMA Safety Manual | ALMA-10.08.00.00-011-C-MAN |
| [AD 04] | Electrostatic Discharge Control Program | OPER-00.00.00.00-0021-A-PRO |
| [AD 05] |  |  |
| [AD 06] |  |  |
| [AD 07] |  |  |

Table 21.  Applicable Documents for this document

## Reference Documents

| Number | Document Title | Reference |
| --- | --- | --- |
| [RD 01] | APP Project Plan | ALMA Phasing Project, latest release |
| [RD 02] | iMaser™ 3000, Installation, Operation & Maintenance User Manual, Issue 1.7, 28-May-2010 | T4S-MAN-0012, available from www.T4Science.com |
| [RD 02] | 64-Antenna Correlator Maintenance Manual | ALMA-60.00.00.00-070-B-MAN |
| [RD 03] | GPS Receiver User Manual | CD Part Number 098-00116-000 Rev. C available from Symmetricom and supplied with data sheets |
| [RD 04] | MK6 Recorder User Manual |  |
| [RD 05] | Interface Control Document Between ALMA Phasing Project And ALMA Computing | ALMA-05.11.00.49-0004-B-ICD |
| [RD 06] | ALMA Phasing Project Hydrogen Maser Maintenance Plan | ALMA-05.11.21.01-0004-A-PLA |
| [RD-07] | APP Optical Fiber Link maintenance manual | ALMA-05.11.40.01-0001-A-xxx (TBD |
| [RD-08] | APP Correlator Upgrades Maintenance Manual | ALMA-05.11.30.05-0001-A-MAN |
| [RD-09] | Mark6 Maintenance | Mark6 Memo Series |

Table 22.  Reference Documents for this document

## Abbreviations and Acronyms

| AC | Alternating Current |
| --- | --- |
| AD | Applicable Document |
| ALMA | Atacama Large Millimeter Array radio telescope |
| AOS | Array Operations Site |
| APP | ALMA Phasing Project |
| APS | ALMA Phasing System |
| ATX | Advanced Technology eXtended (standard for Personal Computers) |
| BE | Back End |
| CAI | Correlator Antenna Input |
| CIC | Correlator Interface Card |
| CRG | Central Reference Generator LRU |
| CVR | Central Variable Reference LRU |
| CVRR | Central Variable Reference Rack |
| DLO | Digital Local Oscillator |
| GPS | Global Positioning Service |
| HMR | Hydrogen Maser Rack |
| ICD | Interface Control Document |
| IPT | Integrated Product Team |
| LLCR | Line Length Corrector Rack |
| LO | Local Oscillator |
| LRU | Line Replaceable Unit |
| LVDS | Low Voltage Differential Signal |
| M&C | Monitor and Control |
| MFS | Master Frequency Standard LRU |
| ML | Master Laser LRU |
| NRAO | National Radio Astronomy Observatory |
| PAI | Preliminary Acceptance In-House |
| PAS | Provisional Acceptance On-Site |
| PDU | Power Distribution Unit |
| PIC | Phasing Interface Card |
| PLOTS | Photonic LO Test Stand |
| PPS | Pulse Per Second |
| PRDR | Photonic Reference Distribution Rack |
| PRR | Photonic Reference Rack |
| RF | Radio Frequency |
| RFI | Radio Frequency Interference |
| SASR | Sub Array Switch Rack |
| TE | Timing Event (a 48-msec timing tick which is the heartbeat of the ALMA control system) |
| TSM | Temperature Sensor Module |
| UPS | Uninterruptable Power Supply |
| VDIF | VLBI Data Interchange Format |
| VEX | VLBI EXperiment |
| VLBI | Very Long Baseline Interferometry |

## Definitions

None so far…

# ALMAPhasing System Description

The purpose of this section is to provide an description of the ALMA Phasing System (APS) and its various components.

## System Overview

The purpose of the APS is to enable ALMA to be part of larger telescope using an observing technique called Very Long Baseline Interferometry (VLBI).  A larger telescope provides the users with higher resolution images of astronomical objects.  VLBI is a technique for combining signals from multiple radio telescopes to make an interferometer with very long baselines.   Since it is physically impossible to interconnect the telescopes with cable, signals from the telescope are recorded and correlated at a special correlator with the capability to play back recordings from multiple telescopes.  Recorders have very limited bandwidth.  Therefore, in cases where a telescope consists of multiple antennas (an interferometer like ALMA for instance), the signals from the multiple antennas must be combined to look as if they come from a single antenna before recording.  This involves “phasing” the antennas so that signals from all antennas are in phase and then “summing” the antennas, i.e., adding the signals from all the antennas together.

A block diagram of the additions to ALMA that are necessary to make it a VLBI telescope are shown in Figure 31.  The blocks that are shaded in blue represent additions to the ALMA system for the purpose of enabling ALMA to participate in VLBI observations.  Each of the block is described in a dedicated section.

## H-Maser

The H-Maser or “hydrogen maser” is the time standard that replaced the Rubidium time standard.  It is shown in the block diagram near the top left of the Figure 31.  A photo of the H-Maser is shown in Figure 32.  The reason that the Rubudium standard had to be replaced is that it is not stable enough over time.  Recall that the signals from the various telescopes are not connected by cables.  If they were, we could have one Central LO and all the data samples would be coherent with one another.  Since all the telescopes have different LOs, they must be as stable in time as possible with respect to each other.  The H-Maser is the most stable frequency standard in existence for the time intervals useful to VLBI.  It uses the intrinsic properties of the hydrogen atom to derive a frequency reference.  Its stability is specified at 2.10-15 in 1000 seconds.  This stability is comparable to 1 second in 63,376,176 years!  For further information, see http://en.wikipedia.org/wiki/Hydrogen_maser

Figure 31.  Block Diagram of the ALMA Phasing System.

Figure 32.  Photo of the H-Maser

## Phasing Interface Card

There are eight Phasing Interface Cards (PIC) in the APS.  A photo of one of the cards is shown in Figure 33.  The purpose of these cards is to format the summed data for recording.  The formatting consists grouping the data into packets and adding time tags, serial numbers and other pieces of useful information to each packet.  A second layer of formatting is also provided; it turns the data stream into a standard 10 Gb Ethernet data stream.  Additional detail can be found in [RD-05].  As can be seen in Figure 33, the design of the card is fairly complex.  It actually consists of three cards.  The largest card is an NRAO custom design and contains the standard correlator microprocessor system and clock circuitry, buffers for the input data and provisions for mounting a daughter card.  This card makes the PIC look like any other control card in the system (e.g., LTA, SCC) to the CCC and Engineering Port computers and makes it possible to re-use a great deal of code.  The large daughter card is a standard off-the-shelf CASPER ROACH2 board manufactured by Digicom.  It contains a large FPGA (under the fan) which does all of the data formatting.  It also contains a Power PC (PPC) which runs a small linux operating system.  The PPC’s main task is to load the FPGA personality after the ROACH2 board is powered up.  The PPC may be accessed via the site network.  It is possible to monitor the ROACH2 board via a custom interface which is accessible via login or Python scripts.  There is a daughter card mounted on the ROACH2 called the SFP+ card.  Its function is to connect the FPGA to an optical fiber for transmission of 10 GbE frames.  A 10GbE transceiver, which translates the 10GbE signal from electrical to optical is housed in the card cage of the SFP+ card.

Figure 33.  Photo of a PIC.

## Fiber Mux and Fiber Demux

The purpose of the Fiber Mux and Fiber Demux is to concentrate all the data produced by the APS onto one optical fiber.  The two units are identical.  A photo of the unts is shown in

Figure 34.  Photo of the Fiber Mux and Fiber Demux.

# Module-level maintenance procedures

APP has produced a hierarchy of maintenance manuals.  This manual covers system-level maintenance procedures while module level manuals detail procedures specific to individual modules.   Module-level maintenance manuals include [RD-06],  [RD-07], [RD-08] and [RD-09].

# System-level maintenance procedures

System-level maintenance is detailed in the following paragraphs.

APP will provide a system level test in which test data is generated in the Correlator, transmitted through the OFL and recorded in the recorders, exercising all components in the system.  The recorded data is then analyzed for correctness.  This procedure is in development at this time and will be added to this manual in a future revision.

ALMA produces a prodigious amount of monitor data (see http://monitordata.osf.alma.cl/).  APP intends to supply a list of items to inspect and expected value ranges.  The monitoring of the data for the Maser should occur weekly.  Other APP equipment will likely be powered down most of the time.  It should be monitored weekly when powered up.

# Expected Maintenance Costs

This section considers costs associated with the maintenance of APP-provided modules.  These costs can be both in dollars and in time.  The only item which will incur a dollar cost is the Maser maintenance contract.  This is detailed in [RD-06], section 3.  Costs associated with personnel time include the following:

- H-Maser: inspect logs  (0.2 hrs/wk)

- Correlator Upgrades:  run self-test before VLBI experiments (2 hrs/yr)

- All interconnect optical fibers: before VLBI experiments, inspect fibers using fiber inspection probe and clean if necessary (5 hrs/yr)

- OFL: Clean internal fibers every 6 months (2 hrs/yr)

- Recorders: run self-test before VLBI experiments (included in Correlator Upgrades self-test).

Note that some time are in hrs/wk and others in hrs/yr.  These times assume one VLBI session per year.  All APP equipment except the H-Maser is required only for VLBI experiments.  It should be powered down most of the time, minimizing the risk of damage from power transients and SEUs.  It should be powered up about 2 weeks before a VLBI experiment and tested at that time to allow time to recover from any failures.  Note that above, we say to inspect fibers before VLBI experiments while the [RD-07] specifies every 6 months.  The six month interval would apply if VLBI experiments occur more than once per year.